## Slide 1: Introduction To Linux Kernel Development Session 5
Part 5: Kernel Facilities – Memory Management
Khaled Henidak (KAL)

## Slide 2: Instructor
Khaled Henidak (KAL)

## Slide 3: Session Logistics
We will devote 15 minutes at the start of each session to answer questions or to deal with any spillover from the previous session.
There will be a 10-minute break around the start of the second hour
Questions are welcome throughout the session​
Both on the Teams channel as well as live during the session​
All sessions are recorded​

## Slide 4: Last week
Answer questions or deal with any spillover from the previous session.

## Slide 5
Kernel Facilities – Memory Management
Topics Covered:
Linux Mem 101
Allocators Interfaces
Slab allocators
NUMA aware allocators
Lab:
~/class-projects/week5
1. Implement the skeleton of a synthetic device
2. Implement the skeleton of a module to drive the device

## Slide 6: Linux Memory 101

## Slide 7
Four Types of Things that runs on Linux
Code that runs
in a process
Code that runs in kernel space executing a syscall on behalf of a process
Kernel thread, kworker (top half)
Interrupt handler
(bottom half)
Soft irq

## Slide 8: Process Memory
Each process gets a full 64bit int of address space.
General placement is static, but actual is randomized (i.e, x40..0 is random).
Kernel is mapped in all processes.
struct thread_task saved at the top of the address space (bottom of kernel stack) allowing kernel to do quick lookup to current process.
A Process: Modern Kernel View
Source: Computer Systems: a programmer’s perspective

## Slide 9: Process Memory
Process typically call:
  brk(2) which increases uninit-ed data segment (the .bss) which effectively increases the heap size.
  mmap(2) by using anonymous/private maps process maps parts of its memory space to physical memory.
  Both are done via libc malloc(3) which makes the decision internally.
Memory is allocated in chunks of <page-size> and mapped to physical memory. A continues space in virtual mem != continues space in physical memory. Memory is not allocated until it is read/write.
The entire page table is part of task struct – per process – instance (mm_struct as mm member). When scheduling a new task kernel swaps task_struct for current task and accordingly it loads its page table.
Page table translation is done by the CPU via look aside cache. HTLB is a feature that allows allocating a large continues block of physical mem hence it uses less translation calls.
Note: the Page Table is three layers compacted for fast find/translation. Details is beyond the scope of this class
A Process: Modern Kernel View
Heap
Page
Page
Page
Page
…
…
Physical memory
Process memory

## Slide 10: Alloc != Alloc among other things
Contrary to the popular belief `malloc()` does not allocate memory. It it just adds page on the left-hand side of the page table pointing no where. Memory is allocated when you write to them.
Kernel caches a lot of things. As in A LOT OF THINGS:
  Inodes for FS ops
  Page cache for pending-writes, previously read blkdev blocks, read-ahead blkdev blocks.
  Kernel slabs (more on this next session).
  Sizes + flush/reclaim ration are tunable as settings for your kernel(flush can also be triggered manually) . Kernel operates a set of background flusher threads that are triggered when configured cache ratios are met (for pending writes).
Under memory pressure kernel will try to push things out of memory which may result in either FS ops or IO ops. Hence it is perfectly normal for `memset(<target>, 0, <size>)` to result into IO ops under memory pressure.

## Slide 11: Notes on Kernel Memory
Kernel Memory is completely separated from userspace app memory. The only way to copy data from/to kernel is via the following apis
  copy_from_user(void *to, const void *from, unsigned long n);
  copy_to_user(void _user *to, const void *from , unsigned long n);
There are ways used by io_uring via memory maps, discussed later.
Based on the 4 types of code that can run on linux:
  User code task_struct gets replaced before switching context to user thread.
  If the code is kernel mode code running on behalf of user. Then task_struct.mm is already there with all the needed addresses (ready for from/to user copy ops).
  For everything else (kthreads and bottom-half irq handlers) then task_struct.mm will be NULL and kernel will use mm of last ran task (which will be the same for kernel addresses anyway) and since background threads can’t read/write to user memory everything will be fine.

## Slide 12: Before we move any further, a note on memory mgmt
There are finite types of memory ownership in kernel:
  Heap Owned: memory you allocated in your module code for your own use and you are responsible for releasing. Example: temp buffers, ioctl handling, internal state etc.
  Heap Processing: memory that you are operating on but you are not allocating nor releasing (at least in most cases). Example: custom extension to iptables where you are operating on skbuff struct. You may increase it, decrease it or even release it in some cases of failure.
  Heap Received, but not owned: Memory that you have received but you don’t destroy. Example: an empty io request buffer for your blkdev to fill in the request’s response.
  Heap Created, but not owned: Memory that you create but you don’t own it. Example: Your network driver may create skbuff instances push it up the stack but you don’t typically destroy them.
  Stack Memory: created and removed as you the stack frames created and unwind-ed.
Kernel trusts itself. If you used memory before zeroing it out, you will use garbage and you may compromise the security of the system. If you free mem that you don’t own, then you risk panicking the kernel or worse corrupting data.

## Slide 13: Kernel Memory Structure: Stack
Kernel does not perform a lot of magic around its stack management, for obvious performance reasons.
Kernel stack size is One Page for the entire call chain because due to proximity to userspace memory you can easily shoot into it.
Kernel toolchain will tell you if you use more in one func, wack you (kernel panic) if you used more across a call chain
struct whatever {<large # of fields>};
struct whatever records[100];
NO!

## Slide 14: Kernel Memory Structure: Heap
Kernel split memory into zones, these are are also per node (more on this next session):
  ZONE_DMA: To allocate mem for devices that needs to do DMA.
  ZONE_DMA32: to allocate mem for devices that can not address more than 32b
  ZONE_NORMAL: regular memory.
  ZONE_HIGHMEM: for architecture where addressing the entire memory is not possible.
Allocation interfaces _do_ allocate memory. Some return lh and some return rh values of the page table (as we will see later). Generally, they are capped to max sizes. RTFM.
The zone split is architecture dependent e.g., x64 arch can address all memory hence HIGHMEM is always empty.
All allocation interfaces use zone hints. Zone requirements can be fulfilled from other zones. E.g., Normal mem allocation can pull from DMA zone but the inverse is not true.
Notes: ZONE_DMA and ZONE_DMA32 because some devices can’t address beyond certain addresses

## Slide 15: Page Align and Address Align
Page allocation interfaces yields into page allocated memory but not necessarily address aligned memory. IOW if you want to remain within a single call TLB for memory access allocate a single page.
Memory Allocation interfaces yield into address allocation (e.g., ARCH_MALLOC_MIN_ALIGN typically 8 bytes) But they make no guarantees around page alignment and thus TLB lookups. IOW byte by byte walk can span 1+ pages.

## Slide 16: Kernel Memory Allocation Interfaces

## Slide 17: Note on gfp_t flag
All allocation functions takes a flag. The flag controls action, type and zone modifier. There are plenty of __ 2X underscore flags and higher-level flags, most notably. These flags can be combined:
  GFP_ATOMIC: high pri mem allocation, no sleep, no io/fs ops.
  GFP_NOWAIT: as ATOMIC but can fall back to emergency mem reservs.
  GFP_NOIO, GFP_NOFS: allocate without either of ops.
  GFP_KERNEL: general purpose can sleep, can block.
  GFP_USER: allocate for userspace apps.
  GFP_HIGHUSER: allocate from high mem for user apps.
  GFP_DMA: from dma zone.

## Slide 18: Page Allocation
struct page * alloc_pages(gfp_t gfp_mask, unsigned int order)
Allocates 2^order pages, returns a pointer first page.
Unsigned long __get_free_pages(gfp_t gfp_mask, unsigned int order)
Combines alloc_pages & page_address functions
void * page_address(struct page* page)
Returns a pointer to page content
struct page * alloc_page(gfp_t gfp_mask)
unsigned long __get_free_page(gfp_t gfp_mask)
Single page
struct page* get_zeroed_page(gfp_t gfp_mask)
Single page,zeroed
void __free_pages(struct page * page, unsigned int order)
void free_pages(unsigned long addr, unsigned int order)
void free_page(unsigned long addr)
Free pages
Page allocation is the root allocator. All other allocation interfaces are built on top of it. Pages are allocated in sequence. Meaning, alloc_pagec(GFP_KERNEL, 2) will allocate one memory space == 4 pages (4 * 8K), no remapping or clever working. Note page struct v page content pointer. All allocation must be tested for success (e.g., if !(p == alloc_page(GFP_KERNEL))). Page allocation allocates the rh value of the page table, not the lh value of it. Mapping or page_address is needed to convert to a useable mem address.
Because memory is continuous be very wary because your system may have memory but no hole big enough to satisfy the request. Also, note pages are allocated dirty, you must clear them or use zero-ing functions.

## Slide 19: Chunk Allocation
void * kmalloc(size_t size, gfp_t flag)
Allocates sized memory according to gfp_t mask
void kfree(const void * ptr)
Frees memory allocated by kmalloc()
The most common allocation interface. Similar to pages in that it allocate continues space (no remapping). Same gfp_t flag applies. Must also be tested for successful allocation upon return.

## Slide 20: Virtual Allocation
void * vmalloc(unsigned long size)
Allocates size from virtually mapped memory
void vfree(const void * ptr)
Frees memory allocated by vmalloc() function
Rarely used. Memory allocation is not a continues block but similar to userspace. Each page can point to a different page on physical memory. Adds a perf penalty due to look aside cache checks. Mainly used for loading txt section of kernel modules. vmalloc() allocates from ZONE_HIGHMEM however a sister function __vmalloc(unsigned long size, gfp_t mask) can be used to allocate from different zones.
Note kernel configuration allows you to change where vmalloc() from (still high mem but you can control placement).

## Slide 21: Mapping Pages
Pages allocated from HIGHMEM zone are not mapped into kernel address space.
  void * kmap(struct * page): maps the page and return pointer to its content.
  void kunmap(struct *page): unmaps previously mapped page.
If the HIGHMEM zone is empty or already addressable then the function just silently returns success.
Mapping/unmapping call can sleep. For situation where you can’t (e.g., during interrupt handling) kmap_atomic()/kunmap_atomic() can be used. Kernel maintains a set of reserved mapped addressed used by atomic mapping. You should always map and quickly unmap when done. This entire process is referred to as “temporary mapping”.

## Slide 22: Other interfaces
kzalloc() similar to kmalloc() but zeros out memory.
kmalloc_array() kcalloc() for arrays.
krealloc() and krealloc_array() for resizing.
vzalloc() like valloc() but with zeroing.

## Slide 23: Advanced Memory Allocation Techniques

## Slide 24: On the frequency alloc/free
At any point of time Kernel holds massive # of objects. A common example is cached inodes/dentries (usually in span of 100s K objects). These objects are of predetermined sizes.
There is an overhead for alloc()/free() even if little. The overhead is more visible when you call then 100s K times.
The solution: Cache (pool the memory) where free() don’t return memory to system instead it is recycled for future expected reuse.
The obvious issue: is if every module/sub-system implemented their own caching the kernel has no way of asking “nicely” them to release the pooled memory when the system is under memory pressure.

## Slide 25: Kernel Slab Allocator
Originally created by our friends at Sun for Solaris 2.4 (1994). The original paper on USNIX is – still – a fantastic read.
The idea is cache (struct kmem_cache) object, root of object graph with – 1 level - tree of slabs. Each slab is a collection of objects (all share the same size). A good read for internals is here: https://hammertux.github.io/slab-allocator or the code itself (/include/linux/slub_def.h and /mm/slab.h)
Kernel knows about slabs and asks them to release unused memory when it is under mem pressure
Use slabtop(1), /proc/slabinfo, and other tools (e.g., drop caches) to interact with slabs from userspace.
Like all other allocator interfaces slab allocator is built on top of cache allocator.
What should not be on slab? (some of)
  Deterministically sized ring buffers (e.g., rx/tx queues of net device). But a growing list or growing queue is a fair game (though having unbounded growth is a terrible idea).
  One-time global allocations such as telemetry, counters etc.
  A well know count of objects that will remain more or less (use page allocator or kmem_alloc).

## Slide 26: Using The Slab Allocator
What | How
Create a new cache: Name Size Align req Flag SLAB_POISON ¦ SLAB_RED_ZONE ¦ SLAB_HWCACHE_ALIGN Optional ctor as: void *init(void *) that will be called for every allocation if not NULL | struct kmem_cache * kmem_cache_create(const char * name, size_t size, size_t align, unsigned long flags, void (*ctor) (void *));
Allocates from previously created cache. Note the gfp_t flag similar to other allocation interfaces. | void * kmem_cache_alloc(struct kmem_cache * cachep, gfp_t flags);
Returns memory to cache. memory must be used again directly instead use allocation function. | void kmem_cache_free(struct kmem_cache * cachep, void * objp);
Destroys the entire cache. All mem is returned to kernel (e.g., module unload sequence or when it is no longer needed). Must *not* use the any of allocation of freeing function after destroy call | void kmem_cache_destroy(struct kmem_cache * cachep);

## Slide 27: On the locality of memory
CPU Cores don’t operate on “memory” but on L1 cache. Data must be brought into L1 cache before processing. For more about cache line alignment and other fun stuff read: https://people.freebsd.org/~lstewart/articles/cpumemory.pdf
Modern SMP each core (or group of cores .. E.g., socket) is connected to memory controller (and io controller as well). and each controller is connected to part of the memory. Reading from that part is called local mem, other mem is called “remote”. Some are further than others. The entire topology matters in low latency code. Accessing remote memory is more expensive than local.
CPUs collectively using cache coherent approach (details are beyond scope of this class).
Source: https://cloudarchitectmusings.com/2012/12/17/the-impact-of-numa-on-virtualizing-business-critical-applications/

## Slide 28: What does this mean?
Because of cache coherence the only thing kernel mem mgmt provide is facilities around “speed of access”.
The HW view of the system is mapped to a logical view where node == 0..n(CPU) + 0..n(MEM-BUS) + 0..n(IO-BUS). Keeping the topology mapped (closer memory is physically closer). This entire topology can also be emulated for testing.
Each node is memory zoned.
That means
  Default allocation tries to satisfy the allocation from same node, or a close node. Also referred to “hard-coded policy” (not to be confused with other numa policies that are userspace numa policies, its apis or cpusets. More about them here).
  Allocation can be restricted to “node” (increases the failure rate of allocation).
  Allocation be be “per-cpu” Where the same memory –sized- is allocated per cpu.

## Slide 29: Node Specific Allocation
Kernel allocation interface offer *_node interface e.g., kmalloc_node(size, flags, node) or kmeme_cache_alloc_node(cache, flags, node).
Getting node:
  Easy: numa_node_id() function returns the current node you are running on. But keep in mind preemption.
  Common (sequence):
    get_cpu(): gets current cpu and disables preemption.
    CPU_to_node(): maps current CPU to its node
    put_cpu(): resumes preemption.
    Allocate on target node as needed using any of the kernel memory allocation interfaces.
Note: unless the thread is pinned to cpu the kernel can and will remove the thread to other core if the current core is over subscribed and other are ideal-ing.

## Slide 30: Per CPU Allocation
Per CPU allocation helps when there are per core threads running. A common example is counters and ring buffers. Note per CPU allocation allocates only from GFP_KERNEL (here: https://elixir.bootlin.com/linux/v4.2/source/mm/percpu.c#L1080)
Statically
  Use DEFINE_PER_CPU(type, name) (and DECLARE_PER_CPU(type, name) macros
  Use get_cpu_var() and put_cpu_var() (get disables permission. Put reverts it. As you’d expect).
Dynamically
  alloc_percpu(type, name); //macro
  free_percpu(const void*);
  Same get_cpu_var/put_cpu_var can be used to work with allocated memory.

## Slide 31: Appendix
Relevant Things That We Did Not Have Time For

## Slide 32: Memory Management Techniques

## Slide 33: The all-at-once
struct s1{};
struct s2{};
int do_something_fancy() {
struct s1 *o1;
struct s2 *o2;
// allocate all memory at once
void *mem = kmalloc(sizeof(struct s1) +sizeof(struct s2), GFP_KERNEL);
if (!mem){
return 1;
}
memset(mem, 0, sizeof(struct s1) + sizeof(struct s2));
o1 = (struct s1 *)mem;
o2 = (struct s2 *) mem + sizeof(s1);
// do the work
kfree(mem);
return 0;
}

## Slide 34: The one-at-a-time
struct s1{};
struct s2{};
int do_something_fancy() {
int ret = 0;
struct s1 *o1 = NULL;
struct s2 *o2 = NULL;
o1 = (struct s1 *) kmalloc(sizeof(struct s1), GFP_KERNEL);
if (o1 == NULL){
ret = -1;
goto out;
}
memset(o1, 0, sizeof(struct s1));
// do some work with o1
o2 = (struct s2 *) kmalloc(sizeof(struct s2), GFP_KERNEL);
if (o2 == NULL){
ret = -1;
goto out;
}
memset(o2, 0, sizeof(struct s2));
// do some other work with o2
out:
if (o1 != NULL) free(o1);
if (o2 !=NULL ) free(o2);
return ret;
}

## Slide 35: The owner-creator/destroyer-pair
int do_something_fancy() {
// this works well for small stacked objects
// and can also work on heap
struct fancy f = {0};
if (0 != fancy_init(&f)) return -1;
// do work with fancy
// destroy it
fancy_destroy(&f);
// not we are not freeing fancy. but if
// it was allocated on heap then we must
return 0;
}
// some other file
#define BUFF_SIZE 16
struct fancy{
void * buffer
};
int fancy_init(struct fancy *f){
// allocate fancy inner
// this would be an excellent place for asserting
// that the object is created on zero-ed mem
f->buffer = kmalloc(BUFF_SIZE, GFP_KERNEL);
if (f->buffer == NULL){
return -1;
}
// other fields .. following other patterns
return 0;
}
void fancy_destroy(struct fancy *f){
// always.. ALWAYS check
if (f == NULL) return;
// to allow this to work with partial init
// guard every free call
if (f->buffer != NULL) kfree(f->buffer);
// other fields
//not we don't free fancy.. only inner stuff
// owner of fancy is responsible for freeing it
}

## Slide 36: The renter
int do_something_fancy() {
// this works well for small stacked objects
// and can also work on heap
struct fancy f* = NULL;
if (0 != fancy_create(&f)) return -1;
// do work with fancy
// destroy it
fancy_destroy(f);
return 0;
}
// some other file
#define BUFF_SIZE 16
struct fancy{
void * buffer
};
int fancy_create(struct fancy **f){
struct fancy *ff = *(f); // just to make it clearer
// allocate ff following the other patterns
return 0;
}
void fancy_destroy(struct fancy *f){
// always.. ALWAYS check
if (f == NULL) return;
// to allow this to work with partial init
// guard every free call
if (f->buffer != NULL) kfree(f->buffer);
kfree(f);
}

## Slide 37: Kernel Memory Leak Detector
How to Enable: https://www.kernel.org/doc/html/latest/dev-tools/kmemleak.html
How It works:
  Scan – manually triggered via debug fs or kernel apis –previous allocation made by allocators.
  Orphan objects are identified.
  Note:
    Has the possibilities of false positives and false negatives (scan is a point of time).
    Is not not smart enough to understand reference to mid point memory. IOW those who likes to stash things at the first few bytes of an allocated memory but then hold reference to the actual thing will see a lot of false positives.

## Slide 38: Measuring Memory Allocated by A Module
As we stand today there is no easy way (lsmod reports text section of the of the module, remember as `kvmem_alloc()`-ed space).
Possible ways:
  Slabs reports memory usage, built in. Zero effort on you.
  Kprobe-ing kmem_alloc (good luck trying to figure out which is which).
A good rule to have – where it applies:
  The stddev between highest mem usage and lowest mem usage (owned, excluding slabs) by your kernel module should be as little possible.

## Slide 39: Red Zoning, and Poisoning
Kernel slab offers poisoning and red zoning to protect against overflows and makes them easier to identify. Use them!
How to: https://www.kernel.org/doc/Documentation/vm/slub.txt
And use-after-free checks: https://a13xp0p0v.github.io/2020/11/30/slab-quarantine.html

## Slide 40: Thank You!